## Slide 1: Analysis of secure boot through FUSE and through PUF technologies
Prepared By: R Dheeraj

## Slide 2: IMX6 – Secure boot (Process Outline)
CST (Code Signing tool generates a PKI tree)
CSF (Command Sequence File) and image key pairs are generated from the SRK (Super Root Key). Private key stays with CA and the public keys are stored as SRK Table.

## Slide 3: Step 2 – Generate SRK Table
CST
Input: CSF binary File
Output: CSF binary signature
Input: Public key certs
Output: Table of Hash Values of SRK
Input: Public key certs
Output: SRK Table (public keys)

## Slide 4: Step 3
Ensure correct FUSE locations are programmed. *Note this is a one time programmable event
Configure U-Boot to ensure secure boot. Pad Uboot image so that CSF signature data (generated using private key) can be concatenated to boot image.

## Slide 5: Step 4
Hash the public keys from the SRK table and check if the keys match with that in the fuse. If verification successful, root of trust is established.
Fuse
SHA-256
Verify
SHA-256(SRK public keys)

## Slide 6: Step 5
Attach CSF binary file signature to the image.
Check if the CSF binary file is successfully verified using the public key. The CSF contains SRK table, certificates and signatures necessary to validate uboot image (Step 6).
Uboot Image File
CSF Binary File
CSF Signature

## Slide 7: Step 6
Uboot bootloader is signed offline by the image provider using private keys.
imx6 processor verifies Uboot image using corresponding public keys obtained from the CSF binary files.
If successfully verified, uboot loads the Operating System from the NVM to the kernel.

## Slide 8: HAB (High Assurance Boot)
Secure boot involves the chained execution of multiple binary files that are loaded, authentic and are not modified, eventually performing as intended by the user.
Root of trust chain anchored in SRK (RSA Key pair). This is to prevent arbitrary public keys used by attackers to run image signed by themselves.

## Slide 9: HAB contd
This assures integrity and authenticity.
Ultimately, ensures that the target embedded device runs only authorized firmware and uses only authorized configuration data.

## Slide 10: BroadKey software based secure boot (PUF technology)
SRAM PUF
Latest cryptographic instance
bk_start
Reconstruct private key (PA)
bk_create_private_key
Source 1: get from device PUF
bk_get_public_from_private
Get public key (PB)
CSF
Sign with PA
Boot loader U-Boot
Verify with PB
CSF attached with signature
U-boot Certificate
Successful verification
Use Public key to verify
ROM

## Slide 11: Random sources to generate Private keys
Using entropy of device to generate private key or through user defined ECC to generate private keys.
Problem: Keys cannot be reconstructed automatically (as seen in previous slide)
Solution: Encrypt it by using bk_generate_cryptogram and store it in non-volatile memory

## Slide 12: Takeaway
Authenticity and integrity preserved.
No need to verify the root of trust chain through FUSE as the root of trust chain is now the SRAM. Additional hardware (FUSE) not required and cost reduced.
Different set of private and public key pairs can be generated by creating another cryptographic instance based on PUF (bk_stop followed by bk_enroll) or can be randomly generated (stored in non-volatile memory). Flexibility in PUF technology that is not available in FUSE

## Slide 13: Takeaway
Use of ECC (Elliptic Curve Cryptography) in Boradkey as opposed to RSA in HAB. ECC uses lower number of bits (improves performance)
Public key generated will be processed by the OEM and the certificate issued is stored on the non-volatile memory  Better than the traditional way of OEM giving silicon manufacturer keys to embed in FUSE (reduced cost and liability)

## Slide 14: Takeaway
Root key programming can be done at any stage in production chain (flexibility)
No need for sensitive data in non-volatile memory (secure) or on any Flash memory (more secure)
Easily and widely deployable (scalability) which is not available through FUSE

## Slide 15: Conclusion
Broad Key Intrinsic ID technology is flexible, reduces cost, easily deployable and scalable as opposed to FUSE technology.
In the long run, total cost of ownership likely come down as opposed to FUSE.
Recommended product to use: BroadKey Flex-E 256 bit entropy to generate a 256 bit key.